## Slide 1
Microscopy
Exercise 2, pg. 15-30 & pg. 37-38; 47
BSC2010L

## Slide 2
Lab Objectives:
Work with a microscope and adjust it to maximum resolution
Locate and define the parts of the microscope
View Fixed Slides to Practice for Microscope Exam test next week pg. 37-38; 47
Intro to Microscopes Exercise 2, pg. 15-30

## Slide 3: Microscopy – using microscopes to view objects that cannot be seen with the naked eye
Light Microscope
  Binocular dissecting microscope
    View: whole to cells
  Compound light microscope***
    View: inside cell structure
Electron Microscope
  Transmission Electron Microscope
    View: inside organelles to molecule = DNA
    Thin slices of specimen
  Scanning Electron Microscope
    View: surface of bacteria/virus’
    Image of surface of specimen
By Mikael Häggström. "Medical gallery of Mikael Häggström 2014". Wikiversity Journal of Medicine 1 (2). DOI:10.15347/wjm/2014.008. ISSN 20018762. - Own work, CC0, https://commons.wikimedia.org/w/index.php?curid=34138383
By Ltumanovskaya V. Nagibin - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=44661206
By Dartmouth College Electron Microscope Facility - Source and public domain notice at Dartmouth College Electron Microscope Facility ([1], [2]), Public Domain, https://commons.wikimedia.org/w/index.php?curid=24407

## Slide 4: The Compound Scope
Two sets of lenses = compound
  Oculars + Objectives
Two focusing knobs
  Course + Fine
Four objective lenses
  4x, 10x, 40x, 100x
+
1
2

## Slide 5: The Objective Lenses
Scanning Objective (4x)
  Red color band, smallest one
Low-power objective (10x)
  Yellow color band
High-power objective (40x)
  Blue color band
Oil Immersion objective (100x)
  Gray color band
  Only use with oil! Have to carefully clean oil off afterwards!!!!!

## Slide 6: Magnification
Total magnification =
  Examples:
    Under 4x objective – magnification of specimen is 40 x
    Under 10x objective – magnification of specimen is 100x
    Under 40x objective – magnification of specimen is 400x
  Question:
    What is the total magnification under a 36x objective lens?
    360x
oculars
X
objectives

## Slide 7: The Objective Lenses – Focus & Field of View
Field of View

## Slide 8: The Objective Lenses – Focus & Field of View

## Slide 9: Microscopy Procedure pg. 21
  CLEAR YOUR WORKSPACE!
  Put mat on Workstation (in your cabinet)
  Find the microscope # assigned to you in the storage cabinet
  Reach UNDER the storage bag
  Carry the microscope with BOTH hands back to the lab bench by ‘ARM’ and ‘BASE’
  Place scope on mat with power cord facing you.
  DO NOT PLUG IN YOUR SCOPE!
  Turn to page 21

## Slide 10: Meet your Microscope: locate the parts while the instructor points them out
Nose piece
Condenser
Coarse adjustment knob
© Moisey - File:Optical microscope nikon alphaphot.jpg, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=7011479
Notes: Have students get out scopes

## Slide 11: Microscopy Procedure pg. 22
Plug it in, turn on light
    Dimmer switch
    Iris Open
    Condenser Up
    Objective on 4x
    Stage down
Set Oculars
  Pull apart or together
  Find one bright circle, not 2!
  Dim slightly to comfort
  May see Pointer or Ruler
Take out fly or threads slide:
*switch to doc cam: go through how to take out and observe slide, note orientation,
stage clip placement, slide centering with manipulation knobs, rotate stage up.
all BEFORE ever viewing specimen/subject through oculars!

## Slide 12: Focus Specimen (pg. 47)
Use Nosepiece and set to Scanning Objective (4x Red color band)
Place slide on stage
Use coarse adjustment knob to raise stage all the way up.
Focus (both: fine and coarse adjustment knobs) and center
Use Nosepiece and set to Low-power objective (10x Yellow color band)
Focus (only fine adjustment knob)
Use Nosepiece and set to Low-power objective (40x Blue color band)
Focus (only fine adjustment knob)
Rotate Nosepiece “backwards” (not THROUGH OIL lense!!) and set to Scanning Objective (4x Red color band)
Now, you can lower the stage

## Slide 13: Microscopy Procedure
  Take out ‘e’ slide
  Turn to Page 21-24 and we do all steps of “TO DO” together. (drawings on page 24)
e
e
The Letter ‘e’
e
e
e

## Slide 14: Microscopy Procedure
  Take out ‘e’ slide
  Turn to Page 21-24 and we do all steps of “TO DO” together. (drawings on page 24)
e
e
The Letter ‘e’
e
e
e

## Slide 15: Practice Focusing on your own pgs. 37-38; 47
Flip to page 47
  These are the steps you need to do every time you look at a slide
  You may tear this page out now or wait until next week when your instructor will use it to conduct your Microscope Exam. YOU WILL NOT BE ABLE TO LOOK AT THIS SHEET WHILE TESTED, so today is to practice until you have it memorized.

## Slide 16: Practice Focusing on your own pgs. 37-38; 47
To prepare for this exam, please turn to page 37 and practice these steps for each slide listed. Sketch what you see at the power listed for each organism on page 38.
If time is limited, you may continue this exercise next week but know you will be tested on the steps listed on pg. 47 using the slide Paramecium* so make sure you practice at minimum with this slide this week!)
    If you want more time, you may come to open lab any day this week @ Main campus where there is not a class being conducted (check the schedule on Weebly <link>
*

## Slide 17: Today’s Lab pgs. 15-30; 37-38
Read and complete all TO DO’s :
p. 20: Calculate total mag. chart
p. 25: Measure field of view with ruler
p. 27: View/Sketch Fixed mount of elodea leaf
(we will do wet mount next week)
p. 29: Fill in microscope parts
p. 37-38: View/Sketch Fixed Mount organisms
p. 30: Complete Before you go questions
NOTE: Next week is your Microscope Exam!!!! Make sure you are using your lab time wisely today to practice using your microscope in the order listed on pg. 47!
x

## Slide 18: Know this for next Lab!
Know the name and function of organelles found in plant and animal cells.
Know differences between them!
Mitochondrion
Cell wall
Golgi apparatus
Nucleolus
Nucleus
Endoplasmic reticulum
Cell membrane
Chloroplast
© Kornelia Fillmer, CC BY-SA 3.0 https://photos.google.com/share/AF1QipN07w2MVbOkY1hNX55T6HF-k7ab1lO6gNOLMKjICmjl1PLBeSHy1uTuaisGMWJzvg/photo/AF1QipMPjNAnq-0k_A1os3jxfSa2DHqr3CepILIVnYus?key=M09OZm9fc3dYU3p4QXhzUVIzMzhFZmJEMy1sckV3
Large central vacuole

## Slide 19: Know this for next Lab!
Know the name and function of organelles found in plant and animal cells.
Know differences between them!
By Divinemercy (Own work) [CC BY-SA 3.0 (http://creativecommons.org/licenses/by-sa/3.0) or GFDL (http://www.gnu.org/copyleft/fdl.html)], via Wikimedia Commons https://upload.wikimedia.org/wikipedia/commons/5/5f/Animal_Cell_Cross_Section_Model.jpg
Mitochondria
Cell membrane
Golgi apparatus
Nucleolus
Nucleus
Cytoplasm
Endoplasmic reticulum
Lysosome

## Slide 20: Focus Specimen pg. 47
Use Nosepiece and set to Scanning Objective (4x Red color band)
Place slide on stage
Use coarse adjustment knob to raise stage all the way up.
Focus (both: fine and coarse adjustment knobs) and center
Use Nosepiece and set to Low-power objective (10x Yellow color band)
Focus (only fine adjustment knob)
Use Nosepiece and set to Low-power objective (40x Blue color band)
Focus (only fine adjustment knob)
Rotate Nosepiece “backwards” (not THROUGH OIL lense!!) and set to Scanning Objective (4x Red color band)
Now, you can lower the stage