## Slide 1: Life Science Lab BSC 1005L
Lab 2 – The Microscope

## Slide 2: The Dissecting Microscope

## Slide 4: The Objective Lenses
Scanning Objective (4x)
  Red color band, smallest one
Low-power objective (10x)
  Yellow color band
High-power objective (40x)
  Blue color band
Oil Immersion objective (100x)
  Not used in this lab

## Slide 5: Magnification
Magnification = ocular x objective
  Ocular lense is usually 10
  Examples:
    Under 4x objective – magnification of specimen is 40 x
    Under 10x objective – magnification of specimen is 100x
    Under 40x objective – magnification of specimen is 400x

## Slide 6: Microscopy
Using the Microscope
  Find the microscope # assigned to you in the cabinet
  Carry the microscope with BOTH hands back to the lab bench
  Plug it in, turn on light
  Place slide on stage
  Always view specimen on lowest power first!
    Focus and center
  Switch to higher power
    Focus and center, etc.
When done:
  Switch lens to lowest power!!
  Take slide off
  Clean lens with only lens paper
  Turn light off
  Unplug
  wrap cord around base
  Place back in cabinet

## Slide 8: Things to Remember
Be careful with Microscope
Never turn head around!
Always clean lenses with lens paper
  In your drawer
You can clean slides with Kimwipes
Always put slides back in slide box in numerical order!!!!!

## Slide 9
Learn parts of the compound microscope that we will use
Learn how to make a wet mount
  Refer to Figure 2.9
Metric System
  Be comfortable with measurements and know how to do conversions!